## Slide 1: Switched Ethernet and IP
Soheil Abbasloo
Department of Computer Science
University of Toronto
Fall 2022

## Slide 2: Last time: Broadcast Ethernet
Ethernet was invented as a broadcast technology
  Each packet received by all attached hosts
  CSMA/CD for media access control
Current Ethernets are “switched”
  Point-to-point links between switches and to hosts
  No (link) sharing, no CSMA/CD
Today: “Switched” Ethernet

## Slide 3: Why Switched Ethernet?
Ethernet switch
A
B
C
D
Enables concurrent communication
  Host A can talk to C, while B talks to D
  No collisions  no need for CSMA, CD
  No constraints on link lengths, etc.

## Slide 4: The evolution of Ethernet
From the shared media coax cables to dedicated links
From 3 Mbps experimental Ethernet to 400 Gbps
From electrical signaling to optical
Changed almost everything except the frame format
Lesson: the right interface can accommodate many changes
  Evolve the implementation while maintaining the interface (backward compatibility)

## Slide 5
As of Aug 2022,
State-of-the-art Ethernet adaptors clock at 400 Gbps
https://www.nvidia.com/en-us/networking/ethernet/connectx-6/

## Slide 6
400 Gbps Ethernet switches
Cisco Nexus 9364D-GX2A switch
https://www.cisco.com/c/en/us/products/collateral/switches/nexus-9000-series-switches/datasheet-c78-743854.html
64 x 400GbE ports!

## Slide 7: Outline
Routing in switched Ethernet
Forwarding in switched Ethernet
IP

## Slide 8: Routing with Switched Ethernet?
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC

## Slide 9: “Routing” with broadcast Ethernet
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC
Sender transmits frame onto broadcast link
Frame contains destination MAC address
Each receiver’s link layer passes the frame to the network layer:
  If destination address matches the receiver’s MAC address
  Or if the destination addr. is the broadcast MAC address (ff:ff:ff:ff:ff:ff)

## Slide 10: “Routing” with broadcast Ethernet
Ethernet is `plug-n-play’
  A new host plugs into the Ethernet and is good to go
  No configuration by users or network operators
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC

## Slide 11: Routing in “Extended LANs”
Local-Area Network (LAN)
Bridges relay broadcasts from one LAN to the other

## Slide 12: The “Broadcast Storm” Problem
Radia Perlman
Perlman’s idea: eliminate loops in the topology

## Slide 13: Easiest Way to Avoid Loops
Use a topology where loops are impossible!
Take arbitrary topology
Build spanning tree
  Sub-graph that includes all vertices but contains no cycles
  Links not in the spanning tree are not used to forward frames
Only one path to destinations on spanning trees
  So don’t have to worry about loops!

## Slide 14: Consider graph

## Slide 15: A Spanning Tree

## Slide 16: Another Spanning Tree

## Slide 17: Yet Another Spanning Tree

## Slide 18: Spanning Tree Protocol (Perlman‘85)
  Protocol by which bridges construct a spanning tree
  Nice properties
    Zero configuration (by operators or users)
    Self healing
  Still used today

## Slide 19: From Extended LANs to Switched Ethernet

## Slide 20: Switched Ethernet
Constraints (for backward compatibility)
  No changes to end-hosts
  Maintain plug-n-play aspect
Earlier Ethernet achieved plug-n-play by leveraging a broadcast medium
  Can we do the same in a switched topology?

## Slide 21: Flooding (still) leads to loops
1
2
4
3
B
A
C
D
Example: A wants to broadcast a message
A sends packet to 1
1 Floods to 2 and 4
2 Floods to B and 3
4 Floods to D and 3
3 Floods packet from 2 to C and 4
3 Floods packet from 4 to C and 2
4 Floods packet from 3 to D and 1
2 Floods packet from 3 to B and 1
1 Floods packet from 2 to A and 4
1 Floods packet from 4 to B and 2
….
A “broadcast storm” if the network contains a cycle of switches

## Slide 22: A Rejected Solution
Example: A wants to broadcast a message
A sends packet to 1
1 Floods to 2 and 4
2 Floods to B and 3
4 Floods to D and 3
3 Floods packet from 2 to C and 4
3 Floods packet from 4 to C and 2
done!
1
2
4
3
B
A
C
D
Can we have 3 remember that it has already received and flooded the message?

## Slide 23: Spanning Tree Approach
  Take arbitrary topology
  Pick subset of links that form a spanning tree

## Slide 24: You: Design a Spanning Tree Algorithm
Take 5 minutes, design with your neighbors, report back
Goals
  Distributed
  Self-configuring
  Must adapt when failures occur
    But don’t worry about that on first try…

## Slide 25: Algorithm Has Two Aspects
Pick a root:
  Destination to which shortest paths go
  Pick the one with the smallest identifier (MAC addr.)
Compute shortest paths to the root
  No shortest path can have a cycle
  Only keep the links on shortest-paths
  Break ties in some way (so we only keep one shortest path from each node)
Ethernet’s spanning tree construction does both with a single algorithm

## Slide 26: Breaking Ties
When there are multiple shortest paths to the root, choose the path that uses the neighbor switch with the lower ID.
One could use any tiebreaking system, but this is an easy one to remember and implement

## Slide 27: Perlman’s description of her algorithm in her SIGCOMM’85 paper:

## Slide 28: Constructing a Spanning Tree
Messages (Y, d, X)
  From node X
  Proposing Y as the root
  And advertising a distance d to Y
Switches elect the node with smallest identifier (MAC address) as root
  Y in the messages
Each switch determines if a link is on its shortest path to the root; excludes it from the tree if not
  d to Y in the message

## Slide 29: Steps in Spanning Tree Algorithm
Initially, each switch proposes itself as the root
  I.e., switch X announces (X, 0, X) to its neighbors
Switches update their view of the root
  Upon receiving message (Y, d, Z) from Z, check Y’s id
  If Y’s id < current root: set root = Y
Switches compute their distance from the root
  Add 1 to the shortest distance received from a neighbor
If root or shortest distance to it changed, send neighbors updated message (Y, d+1, X)

## Slide 30: Example (root, dist, from)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(3,0,3)
(4,0,4)
(5,0,5)
(6,0,6)
(7,0,7)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,3)
(1,1,3)
(1,3,4)
(1,1,5)
(1,1,6)
(1,3,7)
✗
✗
✗

## Slide 31: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Then, switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Then, switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 32: Example From Switch #4’s Viewpoint
Switch #2 hears about switch #1
  Switch 2 hears (1, 1, 3) from 3
  Switch 2 starts treating 1 as root
  And sends (1, 2, 2) to neighbors
Switch #4 hears from switch #2
  Switch 4 starts treating 1 as root
  And sends (1, 3, 4) to neighbors
Switch #4 hears from switch #7
  Switch 4 receives (1, 3, 7) from 7
  And realizes this is a longer path
  So, prefers its own three-hop path
  And removes 4-7 Iink from the tree
1
2
3
4
5
6
7

## Slide 33: Links on spanning tree
3-1
5-1
6-1
2-3
4-2
7-2
1
2
3
4
5
6
7

## Slide 34: Now which ones are on the spanning tree?
2 is new root
3-2
6-2
4-2
7-2
5-6
2
3
4
5
6
7

## Slide 35: Robust Spanning Tree Algorithm
Algorithm must react to failures
  Failure of the root node
  Failure of other switches and links
  How?
Root switch sends periodic root announcement messages
  Other switches continue forwarding messages
Detecting failures through timeout (soft state)
  If no word from root, time out and claim to be the root!

## Slide 36: Outline
Routing in switched Ethernet
Forwarding in switched Ethernet
IP

## Slide 37: Flooding on a Spanning Tree
Switches flood using the following rule:
  (Ignoring all ports not on spanning tree!)
  Originating switch sends packet out all ports
  When a packet arrives on one incoming port, send it out all ports other than the incoming port

## Slide 38: Flooding on Spanning Tree

## Slide 39: Flooding on Spanning Tree

## Slide 40: But isn’t flooding wasteful?
Yes, but we can use it to bootstrap more efficient forwarding
Idea:
watch the packets going by, and learn from them
  If node S sees a packet from node A come in on a particular port, it knows what port to use to reach A!
  Works because there’s only one path to A
A
1
2
3
S
1
2
3
P
From A

## Slide 41: Nodes can “learn” routes
Switch learns how to reach nodes by remembering where flooding packets came from
  If flood packet from Node A entered switch on port 4, then switch uses port 4 to send to Node A

## Slide 42: General Approach
Flood first packet to node you are trying to reach
All switches learn where you are
When destination responds, some switches learn where it is…
Why not all?

## Slide 43: Learning from Flood Packets
Node A
Node A can be reached
through this port
Node A can be reached
through this port
Once a node has sent a flood message, all other switches know how to reach it….
Node B

## Slide 44: Node B Responds
Node A
Node B can be reached
through this port
When a node responds, some of the switches learn where it is
Node B
Node B can be reached
through this port
Node B can be reached
through this port
Node B can be reached
through this port

## Slide 45: Ethernet switches are “self learning”
When a packet arrives:
Inspect source MAC address, associate with incoming port
Store mapping in the switch table
Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 46: Self Learning: Handling Misses
When packet arrives with unfamiliar destination
Forward packet out all other ports
Response may teach switch about that destination
A
B
C
D

## Slide 47: Hence: Forwarding Rule
When switch receives a packet:
index the switch table using destination MAC
if entry found for destination {
if dst on port from which packet arrived then drop packet
else forward packet on port indicated
}
else flood
forward on all but the port
on which the frame arrived
Why do this?

## Slide 48: Summary of Learning Approach
Avoids loop by restricting to spanning tree
This makes flooding possible
Flooding allows packet to reach destination
And in the process switches learn how to reach source of flood
No route “computation”
Forwarding entries a consequence of traffic pattern

## Slide 49: Strengths of Ethernet’s Approach?
Plug-n-Play: zero-configuration / self-*
Simple
Cheap (?)

## Slide 50: Weaknesses of This Approach?
Much of the network bandwidth goes unused
  Forwarding is only over the spanning tree
Delay in reestablishing spanning tree
  Network is “down” until spanning tree rebuilt
  And rebuilt spanning tree may be quite different
Slow to react to host movement
  Entries must time out
Poor predictability
  Location of root and traffic pattern determines forwarding efficiency

## Slide 51: Outline
Routing in switched Ethernet
Forwarding in switched Ethernet
IP

## Slide 52: Local vs. global delivery
Application
Transport
Network
Data link
Physical
L2
Best-Effort Global Delivery
Best-Effort Local Delivery
L3
Network IP Addresses
IP Packet Forwarding
IP Packet Format

## Slide 53: IP Address (IPv4)
A unique 32-bit number
Identifies an interface (on a host, on a router, …)
Represented in dotted-quad notation
10000000
01100100
00010100
00010100
128
100
20
20
.
.
.

## Slide 54: Grouping Related Hosts
The Internet is an “inter-net(work)”
  Used to connect networks together, not hosts
  Need to address a network (i.e., group of hosts)
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
LAN = Local Area Network
WAN = Wide Area Network

## Slide 55: Scalability Challenge
Suppose hosts had arbitrary addresses
  Then every router would need a lot of information
  …to know how to direct packets toward every host
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
5.6.7.8
2.4.6.8
1.2.3.5
5.6.7.9
2.4.6.9
1.2.3.4
1.2.3.5
forwarding table

## Slide 56: A key trick in computer science . . .
When more scalability is needed . . .
A hierarchical structure can be used

## Slide 57: A familiar hierarchical addressing
M5S 2E4

## Slide 58: A familiar hierarchical addressing
M5S 2E4
Notes: Is the mail destined to Ontario or BC?
Bring it to Ontario office

## Slide 59: A familiar hierarchical addressing
M5S 2E4
Notes: Is the mail destined to downtown or uptown?
Bring it to Downtown office
. . .

## Slide 60: A familiar hierarchical addressing
M5S 2E4
Forward Sortation Area
Local Delivery Unit
We use the same approach for network addresses

## Slide 61: Hierarchical Addressing: IP Prefixes
Network and host portions (left and right)
128.100.20.0/24 is a 24-bit prefix with 28 addresses
Network (24 bits)
Host (8 bits)
10000000
01100100
00010100
00010100
128
100
20
20
.
.
.

## Slide 62: IP Address and 24-bit Subnet Mask
11111111
11111111
11111111
00000000
255
255
255
0
Address
Mask
10000000
01100100
00010100
00010100
128
100
20
20
.
.
.

## Slide 63: Scalability Improved
Number related hosts from a common subnet
  1.2.3.0/24 on the left LAN
  5.6.7.0/24 on the right LAN
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 64: Easy to Add New Hosts
No need to update the routers
  E.g., adding a new host 5.6.7.213 on the right
  Doesn’t require adding a new forwarding-table entry
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
host
5.6.7.213

## Slide 65: A bit of History!

## Slide 66: Classful Addressing
In the olden days, there were only 5 fixed allocation sizes (or classes)
 | Leading bits | Prefix length | Capacity | Start add. | End add.
Class A | 0* | 8 |  | 0.0.0.0 | 127.255.255.255
Class B | 10* | 16 |  | 128.0.0.0 | 191.255.255.255
Class C | 110* | 24 |  | 192.0.0.0 | 223.255.255.255
Class D for multicast groups | 1110* |  |  | 224.0.0.0 | 239.255.255.255
Class E reserved for future | 11110* |  |  | 240.0.0.0 | 255.255.255.255
 | Leading bits | Prefix length | Capacity | Start add. | End add.
Class A | 0* | 8 |  | 0.0.0.0 | 127.255.255.255
Class B | 10* | 16 |  | 128.0.0.0 | 191.255.255.255
Class C | 110* | 24 |  | 192.0.0.0 | 223.255.255.255
Class D for multicast groups | 1110* |  |  | 224.0.0.0 | 239.255.255.255
Class E reserved for future | 11110* |  |  | 240.0.0.0 | 255.255.255.255
UofT has 128.100.0.0/16!

## Slide 67: Classful networking was quite wasteful leading to IP address exhaustion
Issue Class C was too small, so everybody requested class B but class B is too big, which led to wasted space
Solution Classless Inter-Domain Routing (CIDR) introduced in 1993

## Slide 68: Classless Inter-Domain Routing (CIDR)
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network
Network number = IP address + Mask
Written as 12.4.0.0/15

## Slide 69: As of August’22, The internet has 930,000 IP prefixes
https://bgp.potaroo.net/as2.0/bgp-active.html

## Slide 70: How IP address allocation happens?
Again, there is a hierarchy

## Slide 71
Allocates large prefixes blocks to Regional Internet Registries (RIRs)
Africa Asia-Pacific America Latin America Europe
RIRs allocates parts of these prefixes blocks to
Internet Service Providers (ISPs) and large institutions
Internet Corporation for Assigned Names and Numbers (ICANN)

## Slide 72: IP Packet Forwarding

## Slide 73: IP Router
Switching
Fabric
Processor
Adapter
Adapter
Adapter
Adapter
Adapter
Adapter
Data Plane
Control Plane
Implementing routing protocols,
computing routing tables
Forwarding actual packets

## Slide 74: Hop-by-Hop Packet Forwarding
Each router has a forwarding table
  Maps destination address to outgoing interface
Upon receiving a packet
  Inspect the destination address in the header
  Index into the table
  Determine the outgoing interface
  Forward the packet out that interface
Then, the next router in the path repeats

## Slide 75: Separate Forwarding Entry Per Prefix
Prefix-based forwarding
  Map the destination address to matching prefix
  Forward to the outgoing interface
host
host
host
LAN 1
...
host
host
host
LAN
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 76: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  Assume a packet destined to 128.100.20.20 comes at Provider 1
128.0.0.0/8
128.100.17.0/24
128.100.18.0/24
128.100.19.0/24
128.100.20.0/24
Provider 2
Provider 1
128.100.20.20
Port #2
Port #1
IP Prefix | Output
128.100.0.0/16 | Port #1
128.200.10.0/24 | Port #1
128.1.0.0/16 | Port #1
128.100.20.0/24 | Port #2
Provider 1’s Forwarding table

## Slide 77: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  Assume a packet destined to 128.100.20.20 comes at Provider 1
128.0.0.0/8
128.100.17.0/24
128.100.18.0/24
128.100.19.0/24
128.100.20.0/24
Provider 2
Provider 1
128.100.20.20
Port #2
Port #1
IP Prefix | Output
128.100.0.0/16 | Port #1
128.200.10.0/24 | Port #1
128.1.0.0/16 | Port #1
128.100.20.0/24 | Port #2
Provider 1’s Forwarding table
???

## Slide 78: Longest Prefix Match Forwarding
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
128.0.0.0/8
128.100.17.0/24
128.100.18.0/24
128.100.19.0/24
128.100.20.0/24
Provider 2
Provider 1
128.100.20.20
Port #2
Port #1
IP Prefix | Output
128.100.0.0/16 | Port #1
128.200.10.0/24 | Port #1
128.1.0.0/16 | Port #1
128.100.20.0/24 | Port #2
Provider 1’s Forwarding table

## Slide 79: Creating a Forwarding Table
Entries can be statically configured
  “map 128.100.20.0/24 to Port #2”
But, this doesn’t adapt
  To failures
  To new equipment
  To the need to balance load
That is where the control plane comes in
  Routing protocols (next lecture)

## Slide 80: IP Packet Format

## Slide 81: IP Packet Structure
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 82: The version number tells us what other fields to expect, typically it is set to “4” for IPv4, or “6” for IPv6
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 83: The number of 32-bit words in the header, typically set to 5 (20 bytes header) Can be more when “IP options” are used
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 84: Allows different packets to be treated differently, e.g., low delay for voice, high bandwidth for video
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 85: # of bytes in the entire packet, with a maximum of 65 535 bytes
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 86: Supports dividing a large IP packet into fragments … in case a link cannot handle a large IP packet
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 87: Used to identify packets trapped in a loop, and eventually discard them
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 88: The upper-level protocol carried in the packet, “6” for TCP, “17” for UDP
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 89: The sum of all the 16-bit words in the header (does not protect the payload) If header bits are corrupted, checksum won’t match, and receiver discards corrupted packets
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 90: Uniquely identify the source and destination host Why do we need source IP?!
version | header length | Type of service (TOS) | Total Length | 
Identification |  |  | Flags | Fragment offset
Time to Live |  | Protocol | Header Checksum | 
Source IP Address |  |  |  | 
Destination IP Address |  |  |  | 
Options (if any) |  |  |  | 
Payload |  |  |  | 
4 bits

## Slide 91: IP Header: To and From Addresses
Destination IP address (32 bits)
  Unique identifier for the receiving host
  Allows each node to make forwarding decisions
Source IP address (32 bits)
  Unique identifier for the sending host
  Recipient can decide whether to accept packet
  Enables recipient to send a reply back to source

## Slide 92: MAC Address vs. IP Address
MAC addresses
  Hard-coded when adapter is built
  Flat name space of 48 bits (e.g., 00-0E-9B-6E-49-76)
  Like a social insurance number
  Portable, and will stay the same as the host moves
  Used to get packet between interfaces on same network
IP addresses
  Configured, or learned dynamically
  Hierarchical name space of 32 bits (e.g., 12.178.66.9)
  Like a postal mailing address
  Not portable, and depends on where the host is attached
  Used to get a packet to destination IP subnet

## Slide 93: Contrast
IP
  Packets forwarded on all links
  Aggregatable addresses
  Routing protocol computes loop-free paths
  Forwarding table computed by routing protocol
Ethernet
  Packets forwarded on subset of links (spanning tree)
  Flat addresses
  “Routing” protocol computes loop-free topology
  Forwarding table derived from data packets(+SPT for floods)